## Slide 1: RMS Web App – Functional & Technical Overview
Solar-Powered Irrigation Pump Remote Management System

## Slide 2: Functional Overview
- Device Management (Register, Assign, Upload)
- Real-time Monitoring (Status, Charts, Alerts)
- Command Execution (Read/Write Modbus Addresses)
- Historical Data Visualization and Export
- Configuration Templates for Standardized Setup
- Alert and Fault Logging
- Secure User Authentication and Profile Management

## Slide 3: Technical Overview
- Frontend: React (Vite), React Bootstrap, React Router, Redux Toolkit
- Forms: React Hook Form + Yup validation
- Backend: Express.js REST API
- Database: MySQL (Prisma ORM)
- MQTT Broker: EMQX hosted at mqtt.macsoftautomations.in
- MQTT Topics: device/{imei}/data, /commands, /response
- Background Services: Node.js MQTT subscribers (ETL, command handler)
- Export: Excel, PDF (future)
- Deployment: VPS / Cloud / Docker (planned)

## Slide 4: High-Level Data Flow
1. Device boots and requests MQTT credentials via HTTP
2. RMS returns broker host, credentials, and topics
3. Device publishes telemetry every 15 minutes to EMQX
4. Background listener subscribes, logs data to DB
5. Web app retrieves and visualizes data
6. Commands are sent from UI via MQTT, responses logged
7. Users view device health, logs, and send config commands